## Slide 1
Network visualization and automation
EuroPython 2017 - Rimini
Network visualization and automation
EuroPython 2017
Antoine Fourmy

## Slide 2
Telecommunication network :
  Networking devices
  Transmission links

## Slide 3
Router
Nokia 7705 SAR
Nokia 1830 PSS
Optical switch
Nokia antenna
Antenna

## Slide 4
Ethernet (10G)
Optical fiber

## Slide 5
Forwarding decision
Electrical – Optical conversion
+
Wavelength multiplexing (WDM)
Microwave transmission

## Slide 6
5620 SAM (Nokia)
U2000 (Huawei)
OneControl (Ciena)
Network Management System (NMS) are provided by equipment manufacturers :
Network visualization
Network inventory
Network provisioning
Network supervision
Network automation (not always)

## Slide 7
Network topology
Drawing of the associated network

## Slide 8
GPS coordinates
Drawing algorithm

## Slide 9
We need :
A GUI programming framework (tkinter)
A widget for drawing (Canvas)
A method to draw polygons

## Slide 10
Shapefile (.shp)
Polygons
Multipolygons

## Slide 11
Shapes extraction
shapefile module
(pyshp)
Shapefile (.shp)

## Slide 12
Polygons and multipolygons
Extract the polygons of a multipolygon
shapely module
Polygons only

## Slide 13
Point on the earth
(longitude, latitude)

## Slide 14
Point on the earth (3D) (longitude, latitude)
Point on a plan (2D)
(projected x, projected y)

## Slide 15
Mercator
Convert geographic coordinates into projected coordinates :
pyproj
Azimuthal orthographic

## Slide 16
We need :
A GUI programming toolkit (tkinter)
A widget to create polygons (tkinter’s Canvas)
A file that contains the map coordinates (shapefile)
A library to read shapefiles (pyshp)
A library to convert multipolygons into polygons (shapely)
A library to convert geographic coordinates into projected coordinates (pyproj)

## Slide 17
SSH/Telnet
NETCONF/YANG (multi-vendor, IETF)
Network programmability using YANG / NETCONF
Puppet, Chef, Saltstack, HPNA
Configuration management tools
Vendor-specific solution
Ansible
Paramiko
Netmiko
Exscript
OSS protocols: TL1, SNMP (pySNMP)

## Slide 18
Run Dijkstra’s algorithm to find the Shortest Path Tree
Create the routing table: (destination outgoing interface)
A router…
(applies to link state protocols like OSPF and IS-IS)

## Slide 19
Allocate names to all interfaces
Allocate IP addresses to all interfaces
Choose a protocol (RIP, OSPF, IS-IS, …)
1
2

## Slide 20
Generate the configuration
Create of the routing tables
4
5

## Slide 21
pyNMS
https://github.com/afourmy/pyNMS
Open-source (GPLv3)
Vendor-agnostic
Tkinter-based GUI (possible switch to PyQT)
No stable release yet (some bug fixing needed)

## Slide 22
Visualization
Emulation (Mininet, pox)
Force-based algorithms
Map drawing
Simulation
Routing
Automatic configuration generation
Capacity planning
Failure simulation
Automation
Optimization
Linear programming (cvxopt)
Metaheuristics

## Slide 23
pyNMS
pyGISS (MIT)
https://github.com/afourmy/pyGISS

## Slide 24
https://github.com/afourmy/pyNMS
https://github.com/afourmy/pyGISS
https://github.com/afourmy/EuroPython-2017
https://github.com/Toblerity/Shapely
https://github.com/jswhit/pyproj
https://github.com/knipknap/exscript
https://github.com/ktbyers/netmiko
https://github.com/ansible/ansible
Thank you